## Slide 1: Course: ECE249
Basic Electrical & Electronics Engineering
Unit-IV
Transistor (PNP & NPN)

## Slide 2: Outline
Basics
Construction
Principal of operation
Important Terminologies, Configurations
Characteristics
Advantages, Applications

## Slide 3: Basics
A transistor is a semiconductor device with three terminals, capable of amplification and switch.

## Slide 4: PNP & NPN Transistors & Symbols

## Slide 5: Transistor Construction
Connecting TWO diodes back to back
TWO PN junctions
THREE terminals are drawn out of the construction
The way the P & N materials are arranged results in PNP or NPN transistor
PNP – N-type material between TWO P-type material
NPN – P type material between TWO N-type material

## Slide 6: Cont…

## Slide 7: Transistor Terminals
Emitter – This segment is on the left side of the transistor. It is moderately sized and heavily doped. The function of it is to supply a number of majority carriers i.e., either electrons or holes. (Emits electrons, also called as emitter) indicated with a letter symbol E.
Base – The middle segment/center of the transistor. It is thin and lightly doped. The main function of this is to pass the majority carriers from emitter to the collector. Indicated with a letter symbol B.

## Slide 8: Cont…
Collector – This segment is on the right side of the transistor. It is larger than the Emitter & Base and is moderately doped. The name implies that its function is to collect the carriers. This is indicated by letter symbol C.

## Slide 9: Cont…
The Arrow-Head indicates that it is an emitter.
Collector of the transistor has made large enough that, it dissipates greater power.
Due to specific function of the emitter and collector they are not interchangeable
Hence terminals are always kept properly while using it.
A notch is always present near emitter terminal.
Terminals can also be identified using multimeter.

## Slide 10: Transistor Biasing
Transistor consists of (1) Emitter-Base Junction (2) Collector – Base Junction
Biasing is controlling the operation of the circuit by providing power supply.
W.K.T Forward Bias and Reverse Bias
Emitter-Base junction is always forward biased, as the emitter resistance is very small.
Collector-Base junction is always reverse biased, and the resistance offered is bit higher.

## Slide 12: Cont…
Hence the name TRANSFER-RESISTOR (TRANSISTOR)
Small Forward Bias & High Reverse Bias
The direction of current indicated in the circuits above, also called as the Conventional Current, is the movement of hole current which is opposite to the electron current.
Current directions in the emitter can be observed.

## Slide 13: Principle of Operation - PNP

## Slide 14: Cont…
Emitter-Base Junction Forward Bias, Collector-Base Junction is Reverse Bias
VEE provides a positive voltage to the emitter – repels the holes in the p-type material – those holes cross the emitter-base junction to reach the base region.
Very few holes recombine with electrons in the N-type base region.
This provides a low base current called IB.
The remaining holes cross the collector-base junction, to constitute collector current IC, which is the hole current.

## Slide 15: Cont…
As a hole reaches the collector terminal, an electron from the battery negative terminal fills the space in the collector.
This flow slowly increases and the electron minority current flows through the emitter, where each electron entering the positive terminal of VEE, is replaced by a hole by moving towards the emitter junction. This constitutes emitter current IE.

## Slide 16: Cont…
In summary,
The conduction in a PNP transistor takes place through holes.
The collector current is slightly less than the emitter current.
The increase or decrease in the emitter current affects the collector current.

## Slide 17: Principle of Operation – NPN

## Slide 18: Cont…
Emitter-Base Junction forward Biased, Collector-Base junction Reverse Biased
The voltage VEE provides a negative potential at the emitter which repels the electrons in the N-type material and these electrons cross the emitter-base junction, to reach the base region.
There a very low percent of electrons recombine with free holes of P-region.
This provides very low current which constitutes the base current IB. The remaining holes cross the collector-base junction, to constitute the collector current IC.

## Slide 19: Cont…
As an electron reaches out of the collector terminal, and enters the positive terminal of the battery, an electron from the negative terminal of the battery VEE enters the emitter region.
This flow slowly increases and the electron current flows through the transistor.
The conduction in a NPN transistor takes place through electrons.
The collector current is higher than the emitter current.
The increase or decrease in the emitter current affects the collector current.

## Slide 20: Transistor Configuration
Based on the connections, transistor configuration is classified as
  Common Emitter Configuration
  Common Base Configuration
  Common Collector Configuration (Emitter Follower)

## Slide 21: - NPN
Common Emitter

## Slide 22: Cont… for PNP

## Slide 23: Common Base
Two terminals are needed for input and two terminals for output. Transistors have three terminals, so one terminal have to be taken as common terminal for both input and output.
In Common Emitter configuration, emitter terminal is taken as common for both input and output.
So input is given between base and the emitter terminals and output is taken between collector and emitter terminals.
This is the most commonly used configuration.

## Slide 24: Cont…
Input voltage VBE is applied between base and emitter terminals and output voltage VCE is applied across emitter and collector.
The output current IC is taken across the emitter and collector terminals.
The input side is forward biased and the output side is reverse biased.

## Slide 25: Cont…
Emitter base region acts like forward biased diode and so the depletion region is very small.
Emitter collector region acts like reverse biased diode and the depletion region is large.
The input current IB is measured in µA because the base region is very lightly doped.
The input and output impedance are moderate in common emitter configuration and thus the current and voltage gain is moderate and the power gain is high.
So this configuration is widely used for amplification.

## Slide 26: Input Characteristics – CE config

## Slide 27: Cont…
Input characteristics are the relationship between the input current and the input voltage keeping output voltage constant.
Here the input current is the base current IB, input voltage is base emitter voltage VBE and the output voltage is collector emitter voltage VCE.
First the output voltage VCE is kept at zero and the input voltage VBE is gradually increased and the input current IB is noted. Then again the output voltage VCE is increased like 10V, 20V and kept constant and by increasing the input voltage VBE, the input current IB is noted.

## Slide 28: Cont…
From the results it is observed that when the input voltage VBE is increased initially there is no current produced, further when it is increased the input current IB increases steeply. When the output voltage VCE is further increased the curve shifts right side.

## Slide 29: Output Characteristics – CE Config

## Slide 30: Cont…
Output characteristics is the relationship between the output current and the output voltage keeping input current constant.
Here the values of output current IC and the output voltage VCE is noted keeping input current IB constant.
In active region when the output voltage is increased there is very slight change in the output Current.
The curve looks almost flat in the active region. Cut off region is the region where the input current is below zero. When both the junctions are forward biased, it is in saturation region.

## Slide 31: Common Base Config. - PNP

## Slide 32: Common Base Config - NPN

## Slide 33: Input, Output Characteristics of CB config.
https://www.learnelectronicswithme.com and learn from it.
Left it as a Work to Students
Future discussion in the class session

## Slide 34: Common Collector Config – CC, NPN

## Slide 35: Common Collector Config – CC, PNP

## Slide 36: Input, Output Characteristics of CC config.
https://www.learnelectronicswithme.com and learn from it.
Left it as a Home Work
What is the alternate name for Common Collector configuration?
Future discussion in the class session

## Slide 37: Advantages of Transistor
High voltage gain.
Lower supply voltage is sufficient.
Most suitable for low power applications.
Smaller and lighter in weight.
Mechanically stronger than vacuum tubes.
No external heating required like vacuum tubes.
Very suitable to integrate with resistors and diodes to produce ICs.

## Slide 38: Applications of Transistor
As an Amplifier
As a Switch
Used in Integrated Circuits (ICs)